## Slide 1: Ns Tutorial: Case Studies
John Heidemann (USC/ISI)
Polly Huang (ETH Zurich)
March 14, 2002

## Slide 2: Road Map
Simple examples
  TCP
  web traffic
Case Study
  Impact of HTTP and TCP parameters to Web performance
  Hidden structure behind aggregated Web traffic
Provide an entry point
Show case ns’s functionality and relevance to the CN program

## Slide 3: Presentation Style
Slides
Script walk-through
Live demos with nam (Network AniMator)

## Slide 4: Example I: TCP
set ns [new Simulator]
set n0 [$ns node]
set n1 [$ns node]
n0
n1
set ftp [new Application/FTP]
$ftp attach-agent $tcp
$ns at 0.2 "$ftp start"
$ns at 1.2 ”exit"
$ns run
$ns duplex-link $n0 $n1 1.5Mb 10ms DropTail
set tcp [new Agent/TCP]
set tcpsink [new Agent/TCPSink]
$ns attach-agent $n0 $tcp
$ns attach-agent $n1 $tcpsink
$ns connect $tcp $tcpsink

## Slide 5: Example II: Web Traffic
A Web session – a series of page downloads
  Number of pages
  Inter-page time
  Page size (number of embedded objects)
  Inter-object time
  Object size (KB)
5 random variables

## Slide 6: Case Study I: Web Performance
Impact of TCP and HTTP parameters
Try to answer:
  Will the proposed changes work in a variety of conditions?
  Should TCP Sack be deployed?
  Should persistency or pipelining be deployed?
  Which parameters are more cost effective to tune?

## Slide 7: Methodology
Methodology
  Select performance critical parameters
  Use most commonly used values as the base case
  Tune parameter values to compare to the base case
Toward a systematic and exhaustive evaluation
Enabled by ns
  rich library of workload and protocol implementations
  Contributed code from a huge user/developer community

## Slide 8: Parameters and Values
Packet size
  576, 1460
Delayed ack
  on, off
Congestion avoidance
  NewReno, Tahoe, Reno, Sack
Initial retransmission timeout
  3, 6 sec
Timer granularity
  100, 500 msec
Timestamp option
  on, off
Initial window size
  2, 4
Connection type
  persistent, simple, pipelined
Number of parallel connections
  2, 1, 4
TCP
HTTP

## Slide 9: Page Download Time – TCP
Sack, NewReno, Reno, Tahoe, gradually better
Timer-related parameters, no significant impact

## Slide 10: Page Download Time - HTTP
Simple, persistent, and pipelined connections, gradually better
Higher the number of parallel connections, Smaller the range of improvement

## Slide 11: TCP vs. HTTP
TCP
HTTP
Impact of TCP Sack is relatively small.

## Slide 12: Low vs. High loss - TCP
Low loss
High loss
That tiny bit of advantage in TCP Sack disappears in high-loss case.

## Slide 13: Low vs. High loss - HTTP
Pipelining loses its advantage when # of parallel connections is high.

## Slide 14: Preliminary Findings
Will the proposed changes work in a variety of conditions?
  Not really
  TCP Sack and HTTP pipelining
Should TCP Sack be deployed?
  Maybe not, if deployment cost is high
Should persistency or pipelining be deployed?
  Maybe yes, but doesn’t make sense to work with too many parallel connections

## Slide 15: The Real Message
Design decisions need to be validated in the context of the Internet.
Layers of protocols, tremendous amount of unknown dynamics
Simulation tools like ns can help us track the complexity (within a layer or across layers)
Ns en-powers such studies
  A rich library base
  A large community contributing to the base

## Slide 16: Case Study II: Web Traffic
Web traffic is not exact self-similar
How does it diverge from exact self-similar?
Why is there this divergence?

## Slide 17: Self-similarity
Distributions of #packets/time unit look alike in different time scale

## Slide 19: Wavelet Analysis
FFT - frequency decomposition dj
WT - frequency and time decomposition dj,k
k(dj,k2) / Nj  Ej = 2j(2H-1) C
log2Ej = (2H-1) j + log2C
j
log2Ej
Self-Similar

## Slide 20: Global Scaling - Trace
Round Trip Time

## Slide 21: Global Scaling - Simulation

## Slide 22: UDP

## Slide 23: TCP

## Slide 24: Findings
Periodicity emerges at round-trip time scales
That periodicity dominates the traffic behavior at those scales
TCP ack clocking plays a critical role
Need to be cautious when to use or not use mathematical self-similar models

## Slide 25: The Real Message
Proposed (traffic) models need to be validated in the context of the Internet.
Mechanisms can influence Internet characteristics in a surprising way
Simulation tools like ns can help us track the implicit complexity
Ns en-powers such studies
  A rich library base
  A large community contributing to the base

## Slide 26: Concluding remarks
Learning ns
  video recording (huang@tik.ee.ethz.ch)
  on-line tutorials (audio and slides)
  tons of info from the ns web site
Research with ns
  promote sharing and confidence